## Slide 1: 4096-Bit RSA Implementation and Its Side Channel Attack Countermeasures on FPGA
QIN zhou
Advisors: prof. cetin koc, prof. tim sherwood

## Slide 2: RSA Cryptosystem
Well-known public-key cryptosystem1.
  Variables
    Plaintext:
    Public key:
    Ciphertext:
    Secret key:
  Encryption
    , , and are big primes.
Decryption
  , , .
2
Notes: RSA is a very well known public-key cryptosystem. In the most basic scenario, we have User X and User Y. User Y generates both public key (e, n) and secret key (d, n), then he sends the public key to User X. User X uses this public key (e, n) to generate a ciphertext C through M^e mod n and sends it to User Y. User Y uses C^d mod n to get message M. In this way, only User X and User Y knows the message M, and only User Y can decrypt the ciphertext C.
Picture refers No.2 in reference page.

## Slide 3: Why do we make 4096-bit?
To guarantee security, large number is needed .
1024-bit RSA has been cracked3 in 2010.
According to RSA laboratory, 2048-bit is recommended since 1369-bit is possibly being cracked today4.
We believe 4096-bit can be secure for longer time. Our solution can make contributions to the industry.

## Slide 4: Why implement on FPGA (programmable hardware)?
Reduce time usage (clock cycle usage) on large number computing
  CPU today computes 64 bits in one clock cycle while FPGA can compute hundreds of bits in a cycle.
Better security
  Since it is another piece of hardware, normally it looks like a black box to hacker.
  Computation is different compared to CPU implementation, harder to reverse engineering.
Better analysis
  On simulation tool every clock cycle is transparent.

## Slide 5: Basic implementation settings of 4096-Bit RSA ()
The 4096-bit numbers are organized as bits, where is the number of words and is the word length5, .
, . ,
Primary Input:
Secondary Input: , , , ,
Output:
  Using Verilog HDL, a hardware language
  IDE: Quartus II 12.1 64-Bit
  Target Device: Cyclone II EP2C50
    A very resource limited device

## Slide 6: RSA Algorithm: The Binary ModExp (Modular Exponentiation)
find the index of the leftmost in
for down to
  , ) (square)
  if then ) (multiplication)
What is ?

## Slide 7: MonPro: Montgomery Product
  , ()
    To get
    ,
Steps6 of , is odd and , , , no time-consuming modular operation.
  for to
  if then return
  else return

## Slide 8: Details of the Implementation
Three modules: MulAdd, MonPro, ModExp
  MulAdd handles basic multiplication and addition, used by MonPro.
  MonPro does a Montgomery Product, used by ModExp.
  ModExp implementes Modular Exponentiation.
In ModExp, there is a 128-bit input wire for input and 128-bit output reg for output.
All internal states are viewable through output pins
Big numbers are initialized before ModExp computation, through readmemh.

## Slide 9: Details of the Implementation

## Slide 10: Efforts of Fitting Code into Cyclone II EP2C50
Chart: 
| Failure | ModExp 1.0 (Only ModExp, MulAdd two modules) | ModExp 1.1 (Optimized configurations on ModExp 1.0) | ModExp 2.0 (Three modules reimplementation)
Total Logic Elements Used in Percentage (50,528 Logic Elements in Total) | 120 | 89 | 80 | 60
Notes: Failure only shows a rough number that above 100. If the resource usage is above 100%, it is impossible to fit into the device.
Optimized configuration means we optimize the compilation by area (resource usage) while it doesn’t mean the speed is faster.

## Slide 11: Time Usage of Implementation
Chart: 
| 32-bit WordLength | 64-bit WordLength | 128-bit WordLength
Clock Cycles Used to Compute c^15 mod n | 673744 | 175634 | 35478
Chart: Max Frequency (MHz) Achievable by FPGA
| 32-bit WordLength | 64-bit WordLength | 128-bit WordLength
Max Frequency Achivable by FPGA | 71.68 | 49.79 | 31.88
  ,
  if word length increases
Notes: The setting is (also in No.7 in reference):
c = 0x444d9850809f292387a1798fe6addd9e61d9fe398147a8f45f0ef320f7f60e7f75f2bc20a7f5195cde62d43f261908b9ccf719ab2922fbd8dca5b35354a1d50572d6bc20d80d6a1cc2472fd603e9ba024cea2df00a66dc4e21681081399f8a8f10fc9eee0a1727f7ea5f24b6de6fec4b843b2a7d15ab2c21ccc93ff710fce97d786e30efce9b2e70b4d4dfccb7d779cc4b5ca436953c178e61067a8cd7a3283c27e969e2c8bf23fb9a431f7a41c30359dfde228125fb5f3d866d7002091472ad52631db9d17034ce51797350e6256403bf3df0bbf66ac168b4a1ca795718ada2027c013f38018399ee6a8e2f9c19ed348af5890333b5b3cedfec4623ab899605a2939b3b7fa74d8aff88ec827f99d273d5627386528cc241e345ac72eac39204ade7cef37ed2ec2f856f3d95e0ae1a1b6c596216ae0fdbc8a36bcb0167e98363905c053b25fdacbe7ce71b48fba52e5998a33736fd1ac7ce1ad0a6f226bdd974d3b564b08be04c3e5c94938160c6b3ed755a3ac132ae2a201ac902ee25777cf09f9821883744da64cc249558f2ad985fff3e0ba10ac728b4a41865bf350d278d41a8a6e165e049937f411fed1e70e79933a1d1c2ad4ab155c09fcd8f739cd488869bdbd2e72bb5b707120911b3b68b57da54f267dd138266d26d53961058fe8c1d7173e55bc7fdeb31234efe6e6480432aa50f4ec6f0093395d1805142cb6d1dL
d=0xf
n = 0x84c5b4763fe31d0347fc816ac16e2284c10faa4003ba33db73f7ba8e0445d656de3a5db5154ed51212093d26ac512b01f18dd1eed77c96c0084f3dd6415af341ee52bdb6d1020a15d9ed17e3cc0e95ee8d103ed3cc667e971773308cdc6b13ab2e47dc0e959f3a518cfe5cd12d5db79ba2a7ae1f3ac7652ccdf8440407295e4299901c0475491bc354c56c9a9cc9af4ec9546b439f9d01298a449ebe89d9bf020067dba8589890086a17b9af5b569643d037cdff7c240d4969d495dd81355c53f0e642f43328ad088ded3c9691eb79fa5d5f576cdeb8fc4c7b297d0b0e5e18baf320cd576d14475b349aae908fb5262cc703806984c8199921167d8fcf23cae883333218bd91a1b7f03edca7e2dcaa37f463b337d20b5d59db610487c89da11b62397bc701762741bab9f87ff50592859be3cecb8c497c68a8c24d4244ef7febe8e5b4617589a82b5a702cfa93ea5c4ed8f33418f3d4e7115804f92283868a29678a5aa33b6fe5078c5fe8f8dc3bf364eb8ac8ce8a245e6b33138131c541013d0326324dfb695ffb3a1890c78092b4d42b28fef02b9c014ea5ac06d864c2f2e39403560d97dae38d9d643c25fbb230bbd92a4aa2b410d93c4efbc8d60b21fbac78255d6807923986bb968a437d5c8dfc5eda92d864ac5db9d707107e855c384429e821a4c74803e31ba1621582283d15a9ec0806705fca161622bd795fec898fL
r = 0x7b3a4b89c01ce2fcb8037e953e91dd7b3ef055bffc45cc248c084571fbba29a921c5a24aeab12aededf6c2d953aed4fe0e722e112883693ff7b0c229bea50cbe11ad42492efdf5ea2612e81c33f16a1172efc12c33998168e88ccf732394ec54d1b823f16a60c5ae7301a32ed2a248645d5851e0c5389ad33207bbfbf8d6a1bd666fe3fb8ab6e43cab3a9365633650b136ab94bc6062fed675bb6141762640fdff982457a7676ff795e84650a4a969bc2fc8320083dbf2b6962b6a227ecaa3ac0f19bd0bccd752f77212c3696e148605a2a0a893214703b384d682f4f1a1e7450cdf32a892ebb8a4cb65516f704ad9d338fc7f967b37e666dee9827030dc35177ccccde7426e5e480fc123581d2355c80b9c4cc82df4a2a6249efb7837625ee49dc68438fe89d8be454607800afa6d7a641c313473b68397573db2bdbb108014171a4b9e8a7657d4a58fd3056c15a3b1270ccbe70c2b18eea7fb06dd7c7975d69875a55cc4901af873a0170723c40c9b1475373175dba194ccec7ece3abefec2fcd9cdb20496a004c5e76f387f6d4b2bd4d7010fd463feb15a53f9279b3d0d1c6bfca9f268251c72629bc3da044dcf4426d5b55d4bef26c3b1043729f4de045387daa297f86dc679446975bc82a37203a1256d279b53a24628f8ef817aa3c7bbd617de5b38b7fc1ce45e9dea7dd7c2ea5613f7f98fa035e9e9dd4286a0137671L
t = 0x149c1965ad98fa46718523dad5f58f409d89062bd8eda4fdf2066470f135295f07c9917922a964a86e6637fa3ca95da43ef4b1440a12b8ef9518ae092a7c394a6748cb70d58c588c1b98a5e684eecd0d6482cd53c788fa6917f328b41c901b921b9e6229191b68a6de0ae73aa48bb1b97d90a87cd03fbbc4958f626f4a1131523a9a9a285a43a743c95f516a94fb9120578e46c026e95b17ebafa21eb031aa153c4a088ffc15c724fb94efe911f499d4713bc2b69544b8f0565a3bcbc87476039409db1237b42777bc768610a3668dd167329a416f1cd4b76f39db9920e96cfce28601753d3988efd7c2368322eec88afc9227224374a351c79891833b715d01ae06fdfb77efa45d06cdb515499fa60711a738951c5836fd35605d6ab7d595c77acdff93e6b100354e1fd46c8dac7c5ee2276688a89b7b2a71a5acdaa14ea7d579c730582a57f5213bf4e86e41840ab5d8e7aee5bebbc2b0f2bb3810c6183272d1aeed41c012e824ae264f5fc010a19efb05f6b41fca9bc4a0a34b0f89fd1237e4e415995f80cfb6cb06c0a97843a5f817df090edd741e9f2b94c7ae4af92d64dc64dc90e98f4afe5e12a9a96f7d7742d4b94bc352c949d7192d6bf19f25d484432c1e910135f001a401baa22b888c2eef79ce5f386efa550d21bcdfdf4473e04255b841d1a34bdb41d7011500400a06490666572b90f2c573053f82acaa289eL
n0’=0x76640c33df911d333bea2df6a3b18a91

## Slide 12: RSA Simulation Demo

## Slide 13: Side Channel Attacks8: Simple Power Analysis (SPA)
Attacks based on information gained from physical channels.
SPA attack on RSA
Doesn’t work if signals contain too much noise!

## Slide 14: Side Channel Attacks8: Differential Power Analysis (DPA)
Use signal processing and error correction to process records of RSA computation with different variables and exploit the secret key .
Many variations of DPA against RSA.
My attack using DPA
  Record power graph of RSA with different but same other settings; synthesize them to an average graph.
  Record power graph of RSA with different and , synthesize.
  Record power graph of RSA with different and , synthesize.
  Compare three graphs and extract every bit of secret key .

## Slide 15: Side Channel Attacks8: Differential Power Analysis (DPA) against Atomic Algorithm
Let
At step , the attacker
  Already knows bits
  Guesses that next bit
  Chooses messages and computes
    , for
  Prepare two sets
    and
    If
Iterate the attack to find ,…

## Slide 16: Side Channel Attacks10: Timing Attack
Suppose we can measure time precisely; we can try different many times. Goal is to crack entire .
Suppose we have guessed bits correctly, and we want to make a guess on .
Construct two sets of , in first set will trigger subtraction in MonPro if , the other set will not trigger subtraction in MonPro if .
If , we will notice the time difference between two sets, otherwise if , two sets have same time usage distribution!

## Slide 17: Countermeasures: Square-and-Multiply-always
For each bit , ModExp behaves the same. Dummy operation is introduced
Input: , , . Output:
;
for downto do
return

## Slide 18: Countermeasures: Montgomery Powering Ladder
For each bit , ModExp behaves the same. Dummy operation is introduced
Input: , , . Output:
;
for downto do
return

## Slide 19: Montgomery Powering Ladder: Drawback
The time usage may double since dummy operation added, in the worst case scenario ().
Chart: 
| Montgomery Powering Ladder | ModExp 2.0
ClockCyles Used to Compute c^(8000)_(16) mod n | 155628 | 88768

## Slide 20: Countermeasures: Blinding
Idea: do ModExp on blinded value then convert result to decrypted text. The signals in side channel has no meaningful information.
, is a random number and .
Drawback
  Need a random number generator.
  Need to compute an extra ModExp, extra MonPro, and inverse of R.

## Slide 21: Countermeasures: Blinding Implementation
In my implementation, and are given. Only two extra MonPro operations are needed
Chart: 
| Montgomery Powering Ladder | Blinding | ModExp 2.0
ClockCyles Used to Compute c^(8000)_(16) mod n | 155628 | 93512 | 88768

## Slide 22: Future Work
Investigate more side channel attacks.
Create more side channel countermeasures; seek publication opportunity.

## Slide 23: Thank you!
Special thanks to Prof. Cetin Koc and Prof. Tim Sherwood.
Thanks to anyone who supported me during my study in UCSB!

## Slide 24: References
http://en.wikipedia.org/wiki/RSA_(cryptosystem)
http://courses.cs.vt.edu/~cs5204/fall00/protection/publicKey.html
http://www.techworld.com/news/security/rsa-1024-bit-private-key-encryption-cracked-3214360/
http://www.emc.com/emc-plus/rsa-labs/standards-initiatives/key-size.htm
ModExp4096.pdf
Encyclopedia of Cryptography and Security, Volume 1. page 802. https://books.google.com/books?id=UuNKmgv70lMC&pg=PA802&lpg=PA802&dq=monpro+algorithm&source=bl&ots=X7yjmGHko3&sig=s3yVdrKh0zjWMFrfHhf4GyhVGDA&hl=en&sa=X&ei=dlH_VO_nEYyyogTnooG4Bw&ved=0CCAQ6AEwAA#v=onepage&q=monpro%20algorithm&f=false

## Slide 25: References
ICDv2.2.doc
Electronics Laboratories Advanced Engineering Course on Cryptographic Engineering. Lausanne, Switzerland Sep 8-12, 2008. Marc Joye, Thomson R&D, Cesson-Sevigne, France.
Timing Attacks on Implementations of Diffie-Hellman, RSA, DSS, and Other Systems. Paul C. Kocher.
Advanced Engineering Course on Cryptographic Engineering. Lausanne, Switzerland Jun 25-29, 2012. Marc Joye, Technicolor, France.